## Slide 1: Short-Circuit Dispatch Accelerating Virtual Machine Interpreters on Embedded Processors
June 20th 2016
ISCA-43, Seoul, Korea
Channoh Kim†
Sungmin Kim†
Hyeon Gyu Cho
Dooyoung Kim
Young H. Oh
Hakbeom Jang
Jae W. Lee
Sungkyunkwan University, Korea
†Equal contributions
Jaehyeok Kim

## Slide 2: Motivation (1): Today’s Scripting Languages
Already widely used in various application domains
  JavaScript, Lua, Python, R, Ruby, PHP, etc.
  Enabling many complex, production-grade applications
[+] High productivity
  High level of abstraction, flexible type systems, automatic memory management, etc.
[-] Low efficiency
  Dynamic type checking, interpretation/JIT overhead, garbage collection, etc.

## Slide 3: Motivation (2): Emerging Single-Board Computers
Emerging single-board computers for so-called DIY electronics
  Arduino, Raspberry Pi, Intel Edison/Galileo, Samsung ARTIK, etc.
  Platforms for emerging IoT applications
[+] Low cost, low power, small form factor
[-] Severe resource constraints
  Single-core, in-order pipeline running at low frequency
  Limited memory/storage space and power budget
Arduino and Raspberry pi
Intel Galileo and Edison
Samsung ARTIK

## Slide 4: Motivation (3): Scripting Languages + Single-Board Computers
Focus of this work
Productivity benefits for IoT programming
  Ease of programming and testing
  Natural support for event-driven programming model
  Seamless client-server integration (e.g., using HTML5/JavaScript)
But, too slow on IoT platforms
  JIT compilation: not viable due to severe resource constraints
  VM interpreter: wastes CPU cycles for
    Recurring cost of bytecode dispatch
    Dynamic type checks
    Boxing/unboxing objects
    Garbage collection

## Slide 5: Motivation (4): Sources of Inefficiency in Bytecode Dispatch Loop
Bytecode dispatch in VM interpreters
  Uses significant # of dynamic instructions
  Examples on x86-64*: Python (16-25%), JavaScript (27%), CLI (33%)
Two main sources of inefficiency
  Hard-to-predict indirect jump
  Redundant computation
    Bytecode decoding
    Bound check
    Target address calculation
for (;;) {
Bytecode bc = *(VM.pc++);
int opcode = bc & mask;
// interpreter-specific
// bookkeeping code (omitted)
switch (opcode) {
case: LOAD
do_load(RA(bc),RB(bc));
break;
case: ADD
...
default:
error();
}
}
* [CGO’15] Rohou et al., Branch Prediction and the Performance of Interpreters: Don’t Trust Folklore.

## Slide 6: Our Proposal: Short-Circuit Dispatch (SCD)
SCD: Architectural support for fast bytecode dispatch in VM* interpreters
  Key idea: Using part of BTB space as efficient, SW-managed bytecode jump table
  Upon bytecode fetch, BTB is looked up using the bytecode (instead of PC) as key
  If hits: short-circuited to the correct bytecode handler If not: falls back to the original slow path
Key results
  Eliminates most of branch mispredictions and redundant computation
  Incurs minimal hardware cost (0.7%)
* Meant for high-level language VMs (as in “JVM”), but not for system virtualization (as in “VMware”)

## Slide 7: Outline
Motivation and key idea
Short-Circuit Dispatch (SCD)
  SCD Design
  ISA extension
  Example walk-through
  Design issues
Evaluation
Summary

## Slide 8: SCD Design (1): Canonical Dispatch Loop
for (;;) {
Bytecode bc = *(VM.pc++);
int opcode = bc & mask;
switch (opcode) {
case: LOAD
do_load(RA(bc),RB(bc));
break;
case: ADD
...
default:
error();
}
}
redundant
computation
Fetch a bytecode
Execute the bytecode
Decode
Bound-check
Jump address calculation
Jump

## Slide 9: SCD Design (2): Overview
Extend BTB to support two entry types
  Bytecode jump table entries (JTEs)
  Conventional BTB entries
SCD-augmented dispatch loop
  Fetch bytecode and extract opcode
  Look up BTB using the opcode
  if hits: go to <fastpath>
  else: go to <slowpath>
Fetch a bytecode
Execute the bytecode
Decode
Bound-check
Jump address calculation
Jump
Jump and update
<slowpath> no
yes <fastpath>
Look up BTB
Hit?
Fetch &
extract opcode

## Slide 10: SCD Design (3): Overview
Five instructions
  <inst>.op (.op suffix): extracts an opcode from the value of <inst>
  bop (branch-on-opcode): looks up BTB using the opcode for fast dispatch
  jru (jump-register-with-jte-update): jumps and updates BTB with a new JTE
  jte_flush and set_mask: bookkeeping instructions (please refer to the paper)
Three registers
  Rop (Opcode register): holds an opcode to dispatch
  Rmask (Mask register): holds a 32-bit mask to extract an opcode
  Rbop-pc (BOP-PC register): holds the PC value of bop instruction

## Slide 11: ISA Extension (1): <inst>.op
<inst>.op suffix
  Update Rop with the value of <inst>
  Rop ← <inst> & Rmask
Fetch:
...
lw s11  0(a5)
lw.op s11  0(a5)
e.g., ADD r0 r0 r1
0x3f
Opcode(ADD)
Rmask
Rop
s11
value of <inst>
Fetch & extract opcode
Execute the bytecode
Decode
Bound-check
Jump address calculation
Jump and update
<slowpath> no
yes <fastpath>
Look up BTB
Hit?

## Slide 12: ISA Extension (2): bop
bop (branch-on-opcode)
  Look up BTB using the opcode as key
  If hits, PC ← BTB[Rop]
  else, PC ← PC + 4
Target address
BTB entry
BTB entry
BTB entry
BTB entry
B T B
Target (ADD)
Rop
Opcode(ADD)
1 0
bop?
key
PC
J
0
0
0
0
J: JTE bit
1
Fetch & extract opcode
Execute the bytecode
Decode
Bound-check
Jump address calculation
Jump and update
<slowpath> no
yes <fastpath>
Look up BTB
Hit?

## Slide 13: ISA Extension (3): jru
J
0
0
0
0
jru (jump-register-with-jte-update)
  Jump-register & insert a new JTE into BTB
  PC ← Rsrc, BTB[Rop] ← Rsrc
Jump:
jr a5
jru a5
※ a5 == Target (ADD)
Rop
Opcode(ADD)
1 0
bop?
key
PC
Target address
BTB entry
BTB entry
BTB entry
BTB entry
B T B
1
Target (ADD)
J: JTE bit
Fetch & extract opcode
Execute the bytecode
Decode
Bound-check
Jump address calculation
Jump and update
<slowpath> no
yes <fastpath>
Look up BTB
Hit?

## Slide 14: Example Walk-through
SCD eliminates two source of inefficiency in dispatch loop
  Branch mispredictions
  Redundant computation (if it hits in the BTB)
J | Target address
0 | BTB entry
0 | BTB entry
0 | BTB entry
0 | BTB entry
J: JTE bit
B T B
1
Target (LOAD)
Bytecodes
LOAD r0 #1
LOAD r1 #2
ADD r0 r0 r1
LOAD r2 #3
ADD r0 r0 r2
1
Target (LOAD)
1
Target (ADD)
1
Target (ADD)
Script
a = 1
b = 2
a = a + b
c = 3
a = a + c
1
Target (LOAD)
1
Target (LOAD)
1
Target (ADD)
1
Target (LOAD)
miss
hit
miss
hit
hit

## Slide 15: Topics Not Covered in this Presentation
Please refer to the paper for the following information:
Details of pipeline design
Conflict reduction between BTB entries and JTEs
OS context switching
Multiple jump tables
Evaluation against the state-of-the-art software/hardware techniques
Evaluation on higher-performance core (Cortex-A8 class)
Detailed power and area analysis using synthesizable RTL
etc.

## Slide 16: Outline
Motivation and key idea
Short-Circuit Dispatch
Evaluation
  Methodology
  Performance Results on Simulator
  Performance Results on FPGA
  Area and Power Consumption
Summary

## Slide 17: Evaluation Methodology (1): Two Evaluation Platforms
 | Gem5 Simulator | FPGA
ISA | 64-bit Alpha | 64-bit RISC-V v2
Pipeline | Single-Issue In-Order, 1GHz Fetch1/Fetch2/Decode/Execute (4 stages) | Single-Issue In-Order, 50MHz Fetch/Decode/Execute/Mem/WB (5 stages)
Branch Predictor | Tournament predictor 512-entry (global); 128-entry (local) 256-entry, 2-way BTB with RR replacement policy 8-entry return address stack 3-cycle branch penalty | 32B predictor (128-entry gshare) 62-entry, fully-associative BTB with LRU replacement policy 2-entry return address stack 2-cycle branch miss penalty
Caches | 16KB, 2-way, 2-cycle L1 I-cache 32KB, 4-way, 2-cycle L1 D-cache 10-entry I-TLB, 10-entry D-TLB 64B block size with LRU | 16KB, 4-way, 1-cycle L1 I-cache 16KB, 4-way, 1-cycle L1 D-cache 8-entry I-TLB, 8-entry D-TLB 64B block size with LRU

## Slide 18: Evaluation Methodology (2): Workloads
Lua-5.3.0
  47 bytecodes
  35 native instructions for dispatch
  No JIT supported, GC turned off
SpiderMonkey-17.0 (JavaScript)
  229 bytecodes
  29 native instructions for dispatch
  Both GC and JIT turned off
Benchmarks
  11 scripts for each from Computer Language Benchmarks Game*
* http://benchmarksgame.alioth.debian.org

## Slide 19: Overall Speedups on Simulator
Geomean speedups
  Lua: 19.9% (Max: 38.4% for mandelbrot)
  JavaScript: 14.1% (Max: 37.2% for fannkuch-redux)
Chart: Speedup over baseline
| binary-trees | fannkuch-redux | k-nucleotide | mandelbrot | n-body | spectral-norm | n-sieve | random | fibo | ackermann | pidigits | GEOMEAN | binary-trees | fannkuch-redux | k-nucleotide | mandelbrot | n-body | spectral-norm | n-sieve | random | fibo | ackermann | pidigits | GEOMEAN | Lua | JavaScript
 | 1.129 | 1.208 | 1.13 | 1.384 | 1.216 | 1.332 | 1.11 | 1.276 | 1.153 | 1.17 | 1.114 | 1.199 | 1.051 | 1.372 | 1.096 | 1.073 | 1.182 | 1.125 | 1.253 | 1.094 | 1.098 | 1.136 | 1.109 | 1.141
19.9%
14.1%

## Slide 20: Branch MPKI on Simulator
Reduction in branch misprediction rate (in MPKI)
  Lua: 15.0  4.4
  JavaScript: 18.9  13.6
Chart: 
| binary-trees | fannkuch-redux | k-nucleotide | mandelbrot | n-body | spectral-norm | n-sieve | random | fibo | ackermann | pidigits | GEOMEAN | binary-trees | fannkuch-redux | k-nucleotide | mandelbrot | n-body | spectral-norm | n-sieve | random | fibo | ackermann | pidigits | GEOMEAN | Lua | JavaScript
baseline | 10.97 | 15.42 | 20.77 | 17.84 | 11.22 | 26.84 | 9.24 | 19.25 | 12.94 | 10.18 | 19.95 | 15.03 | 27.02 | 17.01 | 27.22 | 16.01 | 16.47 | 20.15 | 16.94 | 19.3 | 15.67 | 14.61 | 22.32 | 18.92
SCD | 5.89 | 6.41 | 9.49 | 1.1 | 2.26 | 7.44 | 3.73 | 7.59 | 3.26 | 1.12 | 18.87 | 4.43 | 24.91 | 6.59 | 29.56 | 15.62 | 7.43 | 15.64 | 6.97 | 17.75 | 13.38 | 8.65 | 23.61 | 13.61
Branch misprediction rate (MPKI)

## Slide 21: Instruction Counts on Simulator
Reduction in dynamic instruction count
  Lua: 10.2% (Max: 15.4% for random)
  JavaScript: 9.6% (Max: 15.9% for fannkuch-redux)
Chart: 
| binary-trees | fannkuch-redux | k-nucleotide | mandelbrot | n-body | spectral-norm | n-sieve | random | fibo | ackermann | pidigits | GEOMEAN | binary-trees | fannkuch-redux | k-nucleotide | mandelbrot | n-body | spectral-norm | n-sieve | random | fibo | ackermann | pidigits | GEOMEAN | Lua | JavaScript
SCD | 0.932 | 0.9 | 0.936 | 0.849 | 0.901 | 0.873 | 0.905 | 0.846 | 0.916 | 0.919 | 0.91 | 0.898 | 0.947 | 0.841 | 0.926 | 0.943 | 0.883 | 0.89 | 0.852 | 0.933 | 0.916 | 0.914 | 0.907 | 0.904
Normalized instruction counts

## Slide 22: Overall Speedups on FPGA
Geomean speedup
  Lua: 12.0% (Max: 22.7% for mandelbrot)
Chart: Speedup over baseline
| binary-trees | fannkuch-redux | k-nucleotide | mandelbrot | n-body | spectral-norm | n-sieve | random | fibo | ackermann | pidigits | GEOMEAN | Lua
 | 1.1043 | 1.1678 | 1.0867 | 1.2267 | 1.0897 | 1.1387 | 1.1203 | 1.1301 | 1.1148 | 1.093 | 1.0614 | 1.1204
12.0%

## Slide 23: Area and Energy Consumption
Minimal area/power costs (at 40nm technology node)
  Area overhead: 0.72% (0.59% by BTB)
  Power overhead: 1.09% (0.90% by BTB) → EDP improvement: 24.2%
Chart: Area
| Baseline | SCD
Total | 0.671 | 0.672
BTB | 0.019 | 0.023
Chart: Power
| Baseline | SCD
Total | 17.06 | 17.1
BTB | 1.4 | 1.56
BTB
Others
0
0

## Slide 24: Summary
Two main sources of inefficiency in bytecode dispatch loop
  Hard-to-predict indirect jump
  Redundant computation for decode, bound check, and target address calculation
Short-Circuit Dispatch (SCD) effectively eliminates both
  Low-cost architectural support for fast bytecode dispatch
  Using part of BTB as efficient, software-managed bytecode jump table
SCD accelerates production-grade VM interpreters
  Geomean (Maximum) speedups: 19.9% (38.4%) for Lua, 14.1% (37.2%) for JavaScript
  24.2% EDP improvement with only 0.72% area overhead at 40nm technology node

## Slide 25
Q & A

## Slide 26: Sensitivity Study: Small Size of BTB
Significantly outperforms the default(256) even with a small BTB size (64)
Chart: Speedup over Baseline
| 64.0 | 128.0 | 256.0 | 512.0
binarytrees | 1.0844 | 1.1247 | 1.1286 | 1.1634
fannkuch-redux | 1.0526 | 1.172 | 1.2081 | 1.2258
knucleotide | 1.0353 | 1.0772 | 1.1302 | 1.1141
mandelbrot | 1.2455 | 1.3711 | 1.3839 | 1.3789
nbody | 1.0654 | 1.1307 | 1.2158 | 1.2253
spectralnorm | 1.1926 | 1.2403 | 1.3322 | 1.2642
nsieve | 1.016 | 1.1229 | 1.1098 | 1.1235
random | 1.1397 | 1.1506 | 1.2757 | 1.233
fibo | 1.1166 | 1.1179 | 1.1528 | 1.1514
ackermann | 1.0883 | 1.1639 | 1.1701 | 1.1694
pidigits | 1.0291 | 1.0586 | 1.1137 | 1.1851
GEOMEAN | 1.0948 | 1.1546 | 1.1988 | 1.201
Chart: 
| 64.0 | 128.0 | 256.0 | 512.0
binarytrees | 1.0375 | 1.0438 | 1.051 | 1.0597
fannkuch-redux | 1.1821 | 1.2276 | 1.3718 | 1.293
knucleotide | 1.0562 | 1.0444 | 1.0956 | 1.0583
mandelbrot | 1.0306 | 1.0527 | 1.0731 | 1.0742
nbody | 1.1153 | 1.1532 | 1.1816 | 1.175
spectralnorm | 1.0707 | 1.0831 | 1.1254 | 1.1261
nsieve | 1.0771 | 1.137 | 1.2526 | 1.2252
random | 1.0553 | 1.0776 | 1.0939 | 1.0903
fibo | 1.0742 | 1.1018 | 1.0982 | 1.0971
ackermann | 1.1098 | 1.1542 | 1.1363 | 1.1456
pidigits | 1.0058 | 1.0293 | 1.1094 | 1.0969
GEOMEAN | 1.0731 | 1.0989 | 1.1412 | 1.1289
The number of BTB size
Lua
JavaScript

## Slide 27: Sensitivity Study: Max Cap of JTEs
Chart: Speedups over Baseline
| 8 | 16 | ∞
binary-trees | 1.1071 | 1.0874 | 1.0844
fannkuch-redux | 1.0712 | 1.0579 | 1.0526
k-nucleotide | 1.0754 | 1.0459 | 1.0353
mandelbrot | 1.2726 | 1.2455 | 1.2455
n-body | 1.0904 | 1.0676 | 1.0654
spectral-norm | 1.1262 | 1.1926 | 1.1926
n-sieve | 1.0887 | 1.016 | 1.016
random | 0.9574 | 1.1397 | 1.1397
fibo | 1.1391 | 1.1166 | 1.1166
ackermann | 1.0883 | 1.0883 | 1.0883
pidigits | 1.0789 | 1.0356 | 1.0291
GEOMEAN | 1.0974 | 1.0974 | 1.0948
Chart: 
| 8 | 16 | ∞
binary-trees | 1.0425 | 1.0442 | 1.0375
fannkuch-redux | 1.1776 | 1.1796 | 1.1821
k-nucleotide | 1.0605 | 1.0644 | 1.0562
mandelbrot | 1.0362 | 1.0356 | 1.0306
n-body | 1.1247 | 1.1221 | 1.1153
spectral-norm | 1.0841 | 1.0845 | 1.0707
n-sieve | 1.1853 | 1.172 | 1.0771
random | 1.0614 | 1.0697 | 1.0553
fibo | 1.0929 | 1.0783 | 1.0742
ackermann | 1.1365 | 1.1257 | 1.1098
pidigits | 1.0253 | 1.0224 | 1.0058
GEOMEAN | 1.0921 | 1.0896 | 1.0731
Lua
JavaScript
Capping the maximum number of JTEs in the BTB is not much effected.
  However, some benchmarks get better performance (e.g., n-sieve).
Maximum cap on the number of JTEs

## Slide 28: SCD vs. VBBI (HW) vs. Jump Threading (SW) (1)
Overall speedups over baseline

## Slide 29: SCD vs. VBBI (HW) vs. Jump Threading (SW) (2)
Branch Miss Rate
Normalized instruction count

## Slide 30: SCD vs. VBBI (HW) vs. Jump Threading (SW) (3)
I-Cache Miss Rate

## Slide 31: SCD vs. VBBI (HW) vs. Jump Threading (SW)
Chart: 
| Lua | JS
J-threading | 0.984 | 1.073
VBBI | 1.088 | 1.053
SCD | 1.199 | 1.141
Chart: 
| Lua | JS
J-threading | 0.969 | 0.862
VBBI | 1 | 1
SCD | 0.898 | 0.904
Speedups
Normalized Instructions
Chart: Branch Miss Rates
| Lua | JS
Baseline | 15.03 | 18.92
J-threading | 11.36 | 18.08
VBBI | 3.38 | 10.7
SCD | 4.43 | 13.61
Chart: I-Cache Miss Rates
| Lua | JS
Baseline | 0.28 | 24.32
J-threading | 4.8 | 30.48
VBBI | 0.28 | 22.49
SCD | 0.3 | 24.42